No. 2178-87 CycLoops( Port Bicycle Rack

Bicycle Rack shall be CycLoops Port in the color finish and mounting style selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

Bicycle Rack shall be one-piece 1-1/4 inch x 4 inch mild steel tubing with “D” shaped profile.  Rectangular tube shall not be permitted.  Embedment (-E) mount (permanent) rack shall extend ten inches below finished grade and be drilled prior to application of finish to accept No. 4 re-bar furnished by installing contractor.  Surface mount (-SM) rack shall have welded base plates with two 5/8 inch diameter holes each to accept anchoring devices furnished by installing contractor.

2.  Construction

Bicycle Rack shall be formed into a rectilinear shape and shall be deburred and ground smooth after fabrication.

3.  Finish

Rack shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.